## Slide 1
Design and Evaluation of a Simulation-Based Adaptive Smart Traffic-Light Controller
Final-year project demonstration
Software simulation | dashboard | repeatable benchmarks
Smart Traffic-Light Simulation | 1
Notes: Open by saying the project now focuses on full software simulation rather than physical Raspberry Pi hardware. State the core claim: adaptive timing reduces waiting time or queue length while maintaining zero conflicting-green violations.

## Slide 2
Project problem
Fixed-time traffic lights cannot react to changing demand
A fixed cycle may serve an empty approach while vehicles wait elsewhere.
Adaptive timing can allocate longer green time to the busier movement.
Any timing improvement must preserve amber and all-red clearance.
The project evaluates the algorithm with repeatable simulation data.
5
benchmark scenarios
10
random seeds
0
hardware required
Smart Traffic-Light Simulation | 2
Notes: Explain the decision to move away from hardware: simulation gives repeatable evidence and keeps the project focused on controller logic and safety testing.

## Slide 3
Current scope
A complete simulation project, not a public-road controller
Included | Excluded
Safe four-way phase state machine | Raspberry Pi deployment
Fixed-time and adaptive controllers | GPIO wiring and physical LEDs
Traffic scenarios and detector faults | Camera hardware and real detector calibration
SQLite logging, FastAPI, dashboard | Pedestrian and emergency vehicle phases
Benchmark CSV, charts, report exports | Public-road operation
Smart Traffic-Light Simulation | 3
Notes: Use this slide to make the scope clear. The project is still complete because it implements the algorithm, simulator, dashboard, tests, and evaluation artifacts.

## Slide 4
Implementation architecture
The controller stays separate from simulation, storage, and UI
Layer | Purpose | Main files
Domain | Signal phases, timing, safety checks | src/trafficlight/domain/
Simulation | Queues, scenarios, faults, benchmarks | src/trafficlight/simulation/
Storage | SQLite run, event, detector, metric logging | src/trafficlight/storage/
Interface | CLI, FastAPI, WebSocket dashboard | src/trafficlight/main.py, api/, dashboard/
Same controller code is used by the CLI, API, dashboard stream, and benchmark scripts.
Smart Traffic-Light Simulation | 4
Notes: Point out that the architecture gives a clean explanation for the simulation-only pivot. The algorithm does not depend on GPIO or a physical sensor.

## Slide 5
Controller safety
Adaptive timing changes green duration only
Safe phase sequence
all-red -> NS green -> NS amber -> all-red -> EW green -> EW amber
Fixed and adaptive controllers share the same phase machine.
Every signal state passes through the conflicting-green safety check.
Minimum green protects active traffic from instant switching.
Maximum green prevents one movement from holding green indefinitely.
0
conflicting-green target
Smart Traffic-Light Simulation | 5
Notes: Stress that the adaptive algorithm never directly commands arbitrary lamp colours. It only influences the green phase duration.

## Slide 6
Simulation workflow
Each run advances the intersection in fixed time steps
Generate arrivals from the selected traffic scenario.
Create true queue demand for North, East, South, and West.
Apply detector faults when a fault profile is selected.
Advance the controller and check for unsafe signal states.
Discharge vehicles on green approaches and record metrics.
Experiment settings
Setting | Value
Duration | 300 s
Step | 0.5 s
Seeds | 1 to 10
Scenarios | 5
Smart Traffic-Light Simulation | 6
Notes: Explain that fixed and adaptive benchmark pairs use the same seed, so the arrival trace is identical for the comparison.

## Slide 7
Dashboard evidence
Live simulation and detector faults are visible in the browser
Live queues and moving vehicles
Detector stuck high while real queue is lower
Smart Traffic-Light Simulation | 7
Notes: Use this slide if the live dashboard is slow during the demo. The images are saved Playwright screenshots from the implemented dashboard.

## Slide 8
Benchmark results
Adaptive control reduced mean wait in all scenarios
Chart: Mean wait, seconds
| Balanced | NS-heavy | EW-heavy | NS-burst | Alt peak
Fixed | 265.27 | 281.27 | 290.81 | 287.02 | 301.63
Adaptive | 251.5 | 263.76 | 271.35 | 271.31 | 279.81
5.18%-7.24%
mean-wait improvement range
0
safety violations
Smart Traffic-Light Simulation | 8
Notes: Source: results/dissertation/benchmark_summary.csv and results/dissertation/results_summary.md. The benchmark used 300-second runs, 0.5-second steps, and seeds 1 to 10.

## Slide 9
Fault testing
Bad detector input affects performance, not phase safety
Fault profile | Runs | Completed | Mean wait | Safety violations
none | 10 | 225.80 | 263.76 s | 0
ns-stuck-high | 10 | 228.40 | 258.04 s | 0
ew-stuck-low | 10 | 232.00 | 253.49 s | 0
all-stuck-low-midrun | 10 | 196.60 | 314.48 s | 0
The worst fault profile reduced completed vehicles and increased waiting time, but no test produced conflicting green signals.
Smart Traffic-Light Simulation | 9
Notes: Source: results/dissertation/failure_modes.csv and results/dissertation/results_summary.md. Explain that faults alter demand readings only; they do not set signal colours.

## Slide 10
Conclusion
The simulation supports the adaptive-control claim
The project runs fully in software with no physical hardware dependency.
Adaptive timing reduced mean wait in all five benchmark scenarios.
The adaptive controller completed more vehicles than the fixed-time baseline.
Benchmark and detector-fault experiments recorded zero conflicting-green violations.
The main limitation is the simplified traffic model.
22
tests passing
0
final safety violations
Smart Traffic-Light Simulation | 10
Notes: Close with the limitation clearly: this is a controlled simulation, not a public-road controller. Point to future work such as pedestrian phases, richer detector noise, SUMO validation, and optional hardware adapters.